## Slide 1: Brief Introduction on Global Sensitivity Analysis (GSA) and the SAFE Toolbox for GSA
Dr Valentina Noacco (NERC Knowledge Exchange Fellow)
Dr Francesca Pianosi (Lecturer in Water and Environmental Engineering)
Prof Thorsten Wagener (Professor of Water and Environmental Engineering)
Department of Civil Engineering University of Bristol
Grant Ref: NE/R003734/1
valentina.noacco@bristol.ac.uk

## Slide 2: What is Sensitivity Analysis? and why shall we use it?
Sensitivity analysis (SA) is:
set of mathematical techniques which investigate how uncertainty in the output of a numerical model can be attributed to variations of its input factors.
Benefits:
Better understanding of the model Evaluation of model behaviour beyond default set-up
Model “sanity check”
Does the model meet the expectations (model validation)
Prioritize investments for uncertainty reduction Identify sensitive parameters for computer-intensive
calibration, acquisition of new data, etc.
More transparent and robust decisions Understand main impacts of uncertainty on
modeling outcome and thus on decisions

## Slide 3: How Global Sensitivity Analysis works
INPUT FACTORS included in SA
SIMULATION RESULTS
MODEL
…
INPUT SAMPLING
MODEL EVALUATION
GSA
time
Forcing inputs
Parameters
Spatial resolution
Structure (equations)
time
longitude
latitude
(spatially or temporally distributed)
output 1
pdf
output 2
(…)
OUTPUTS
x1
x2
x3
x5
…
x6
x1 x2 x3 x4 x5 x6
Sensitivity Index
model inputs:
output 1
output 2
x4
x1 x2 x3 x4 x5 x6

## Slide 4
We want to use workflows as a way to transfer expertise.
Often workflows exist only in the users head.
Workflows we produced include guidance on:
how to produce GSA results, and
how to interpret these results.
To this end we have developed an R markdown script to guide in the application and interpretation of SA for models which run in R or Excel.
“And this is where our workflow redesign team went insane.”
We aim to transfer GSA to practitioners and integrate it in their modelling workflows

## Slide 5: GSA Workflow
3. POST PROCESSING
(GSA)
2. MODEL EVALUATION
1. INPUT SAMPLING
EXPERIMENT SETUP
SA steps
User’s choices
Choose the input factors subject to SA
Define other model inputs not subject to SA
Define the scalar model output(s)
Define the input variability space (ranges/PDFs/ …)
Choose the sampling strategy (random uniform, latin hypercube,…)
Choose the sample size (depending on the SA method and number of input factors)
Assess robustness and convergence
Visualize results
Assess credibility of SA
Recommended practice
Choose the SA method(s)
Check model behaviour (and possibly filter out samples)

## Slide 6: What would be the input factors and outputs in a flood inundation model?
x1 x2 x3 x4 x5
time
latitude
y
Input factors
Model output
longitude
MODEL EXECUTION
Savage et al. [2016] (Water Resources Research)
Spatial Resolution
x1
Channel Friction
x2
Floodplain Friction
x3
Discharge (m3s-1)
Time (hours)
Inflow Hydrograph
x4
Digital Elevation Model
x5
(spatially-varying output)
(time-varying output)
or
(Flood extent)
(Maximum water depth)
output 1
output 2

## Slide 7: SA would perturb the input factors… which changes the outputs
x1 x2 x3 x4 x5
time
longitude
latitude
y
Input factors
Model output
MODEL EXECUTION
1
2
3
…
Spatial Resolution
x1
Channel Friction
x2
Floodplain Friction
x3
Inflow Hydrograph
x4
Digital Elevation Model
x5
Discharge (m3s-1)
Time (hours)
1
2
3
…
Savage et al. [2016] (Water Resources Research)
(spatially-varying output)
(time-varying output)
or
(Flood extent)
(Maximum water depth)
output 1
output 2

## Slide 8: …and then estimate Sensitivity Indices
x1 x2 x3 x4 x5
time
longitude
latitude
y
Input factors
Model output
MODEL EXECUTION
1
2
3
…
Spatial Resolution
x1
Channel Friction
x2
Floodplain Friction
x3
Inflow Hydrograph
x4
Digital Elevation Model
x5
Discharge (m3s-1)
Time (hours)
1
2
3
…
(spatially-varying output)
(time-varying output)
or
(Flood extent)
(Maximum water depth)
output 1
output 2
longitude
GSA
x1 x2 x3 x4 x5
Sensitivity Index
model inputs:
output 1
x1 x2 x3 x4 x5
output 2

## Slide 9: Difference between calibration and SA
The ‘calibration’ question: What is the right (or a reasonable) choice for the input factors (i.e. produce a sensible model output)?
The ‘sensitivity’ question: How much varying each input factor contributes to variability of the model output?

## Slide 10: Local vs Global approaches to SA
input factor x2
input factor x3
input factor x1
output variation
input factors
x1
-40 -20 0 +20 +40
x3
x2
y = f(x1,x2,x3)
Local methods analyze sensitivity around some point in the factor space.
Global methods attempt to analyze variability across the full factor space.
Global methods require a good definition of the space you are going to sample
Local methods require a good ‘baseline’ or ‘nominal point’.
input factor x3
input factor x2
input factor x1
x1 x2 x3
Sensitivity Index
1
0.5
0
input factors

## Slide 11: SA allows to achieve different objectives
Ranking
Which input factors have more influence on the model’s response?
Screening
Is there any input factor that has negligible influence on the model’s response?
Mapping
Are there subranges of the input factors that map into “significant” (e.g. extreme) output values?
 specific subranges of the inputs give a flood depth above a threshold
Then possible SA methods:
Regional Sensitivity Analysis
Elementary Effects
Variance Based
Then possible SA methods:
Elementary Effects
Variance Based
x1 x2 x3 x4 x5
Input factors
Model output
Output (e.g. flood depth) above a threshold
Then possible SA methods:
Regional Sensitivity Analysis
Classification and Regression Trees
x1 x2 x3 x4 x5
Sensitivity Index
Model inputs
 x3 > x5 > x4 > x1 > x2
 x4 non influential
x1 x2 x3 x4 x5
Sensitivity Index
Model inputs

## Slide 12: Classification of SA methods
M: number of input factors
Screening
Ranking
Mapping
Type of SA
One At the Time
(OAT)
GLOBAL
Correlation & Regression Analysis
Variance- based
&
Density- based
Multiple-starts perturbation
Monte-Carlo filtering
All At the Time (AAT)
LOCAL
Perturbation & derivatives
SA purpose
Number of model evaluations
~M
~10-100 x M
>100 x M
>1000 x M
d-sensitivity
CC,PCC, SRCC, PRCC,CCA
eFAST , FAST
VBSA
EET
DELSA
RSA
entropy-based
LR (SRC)
CART
Sampling approach

## Slide 13: SAFE (Sensitivity Analysis For Everybody) Toolbox
Developed in 2014 by Pianosi et al.
Over 1300 users in academia and industry
in 50+ countries
Developed in R and Matlab (Python version under way)

## Slide 14: The modular structure of SAFE
POST PROCESSING
MODEL EVALUATION
SAMPLING INPUT SPACE
Elementary Effects Test
Regional Sensitivity Analysis
Variance-Based Sensitivity Analysis
…
GSA steps
 | X |  |  | 
1 |  |  |  | 
2 |  |  |  | 
… |  |  |  | 
N |  |  |  | 
 | 1 | 2 | … | M
sampling
EET
RSA
VBSA
 | Y |  | 
1 |  |  | 
2 |  |  | 
… |  |  | 
N |  |  | 
 | 1 | … | P
AAT_Sampling.m OAT_sampling.m lhcube.m
lhcube_shrink.m
lhcube_extend.m
folders in SAFE Toolbox
EET_indices.m EET_plot.m EET_convergence.m
VBSA_indices.m VBSA_convergence.m VBSA_resampling.m
input samples
output samples
 | S |  |  | 
1 |  |  |  | 
… |  |  |  | 
P |  |  |  | 
 | 1 | 2 | … | M
sensitivity indices
Notes: :: functionalities for assessing robustness of sensitivity estimates
:: tutorial scripts (workflows) to get started > learn by doing > make choices explicit > embed “good practices” > draft for user’ own application

## Slide 15: References and additional material
Website to download SAFE:
https://www.safetoolbox.info/
Introductory paper to SAFE (open access paper):
https://www.sciencedirect.com/science/article/pii/S1364815215001188
A review of available methods and workflows for Sensitivity Analysis (open access paper):
https://www.sciencedirect.com/science/article/pii/S1364815216300287
Example application to handle the issue of epistemic uncertainty (due to climate change) in landslide hazard modelling:
https://www.nat-hazards-earth-syst-sci.net/17/225/2017/nhess-17-225-2017-discussion.html

## Slide 16: Appendix

## Slide 17: Insurance case study
Pricing model based on past losses experience.
It produces a price recommendation for the premium to be charged for a new risk to a given company to cover from all classes of business.
Objective of case study:
Identify where to focus efforts to reduce uncertainty when reviewing the model (i.e. ranking).

## Slide 18: Simplified schematic of pricing model
Pricing model
Output: Loss amount
Claim data Exposure data Cover data
Portfolio and market data
Choice of distribution of inputs
x1. Frequency Trend
x2. Severity Trend
x3. Exposure Trend
x4. Development Pattern
mean
85th percentile
95th percentile
97.5th percentile
Notes: A simplified version is this

## Slide 19: Simplified schematic of pricing model with GSA
Pricing model
Output: Loss amount
Claim data Exposure data Cover data
Portfolio and market data
Choice of distribution of inputs
INPUT SAMPLING
MODEL EVALUATION
POST PROCESSING
Sensitivity index
1
0.5
0
model parameters
Sensitivity analysis
x1 x2 x3 x4
x1. Frequency Trend
x2. Severity Trend
x3. Exposure Trend
x4. Development Pattern
Sampling of inputs

## Slide 20: Results
Summary:
Most influential inputs vary depending on the line of business, therefore this analysis helps to focus efforts to reduce uncertainty and enables to better communicate and outline to the underwriter the uncertainty in the model results due to the assumptions being used.
Varying the inputs within their credible range sensibly increases the variability of the model output, this should be taken into account while making decisions regarding the premium to charge to a client.
There are some unexpected behaviours in how the output responds to changing input values, this highlights areas where to focus when reviewing a policy (addressing these issues could improve the model).

## Slide 21: Varying the inputs within their credible range sensibly increases the variability of the model output
This analysis enables to better communicate and outline to the underwriter the uncertainty in the model results due to the assumptions being used.
Loss amount [million £]
Severity Trend
0 0.2 0.4 0.6 0.8 1
Benefit:
More transparent and robust decisions Understand main impacts of uncertainty on modeling outcome and thus on decisions

## Slide 22: Most influential inputs vary depending on the line of business
We should focus on different inputs to reduce uncertainty depending on the line of business. These inputs could be better estimated from portfolio data of businesses of similar nature.
Line of business 1
Sensitivity index
Line of business 2
Benefit:
Prioritize investments for uncertainty reduction Identify sensitive inputs for computer-intensive calibration, acquisition of new data, etc.

## Slide 23: There are some unexpected behaviours in how the output responds to changing input values
Line of business 1
Line of business 3
Frequency trend and Severity Trend were expected to increase output losses and vice versa for Exposure trend.
Severity trend has an incoherent behaviour for some values.
  this highlights areas where to focus when reviewing a policy, where addressing these issues could improve the model.
Benefit:
Sanity check” of the model
Does the model meet the expectations (model validation)